## Slide 1
Type | HD Encoder + 8VSB Modulator + IP Output(*option)
Inputs | SD/HD-SDI, BNC 75Ω 1ea HDMI 1.4a 1ea (HDCP not supported) Component, YCbCr, 170MHz 12bit ADC, RCA 3ea Composite, CVBS, 3D Comb Filter, RCA 1ea Analog Stereo Audio (Left/Right), RCA 2ea
Video Resolutions | 1920x1080 @ 60p, 59.94p Automatic Convert to interlaced format 1920x1080 @ 60i, 59.94i 1280x720 @ 60p, 59.94p 720x480 @ 59.94i (NTSC) Resolution detect and automatic/manual change support
TS Mux & System | System Delay: 150ms, 200ms, 350ms,650ms TS Bit-rate: 4.5~25 Mbps. Editable TS ID, PMT/PCR/Video/Audio PID.
Video Encoder | MPEG2, H.264 MPEG2 HD/SD (MP@HL/MP@ML), H.264 HD/SD (HP@L4/HP@L3) Bit Rate: (MPEG2) 5Mbps ~ 22 Mbps, (H.264) 3.5Mbps ~ 22Mbps Closed Caption Support
Audio Encoder | MP1L2, Dolby AC3, AAC-LC, HE-AACv2 (Stereo) Bit-rate: 192~384 Kbps (HE-AACv2는 32~96Kbps) Sample Rate: 48KHz Audio Delay: 0~400ms Volume Control: 100%~500%
PSIP Generator | MGT, TVCT Generation Enable/Disable Short name, major and minor channel number setting
  ez-Caster(EN3)
  Specification
  (1/2)

## Slide 2
ASI Output | Connector: BNC 75Ω 1ea Packet Size: 188 Bytes TS Bit Rate: 19.392Mbps
RF Output | Modulation: ATSC(8VSB) Connector: F-Type 75Ω 1ea Output Level : +2~-18dBm (0.5dB Step) Center Frequency Range: 40~999 MHz MER: >36dB Spurious: 60dBc (Relative to Output Level) Phase Noise: VHF 110dBc@20kHz, UHF 95dBc@20kHz
IP Output (*Option) | Ethernet : 10/100Bast-T, half/full duplex Maximum Transmission Unit : 1464~1472 MTU Streaming Protocol : MPEG2-TS/UDP Transport Protocol : UDP, Unicast or Multicast IGMPv1, IGMPv2 support
Management | Front Panel: 4-line text LCD, 6 buttons, Status LED(RGB) Rear USB Port: GUI, Firmware Update
Physical | Dimension: 44(H) X 483(W) X 240(D) (excluding connectors) Operation Temperature: 0~45℃ Weight: 2 Kg Power Consumption: 25W(max.)
  ez-Caster(EN3)
  Specification
  (2/2)